## Slide 1
PTP version 3 in FTI?
Øyvind Holmeide/Markus Schmitz
01/13/2016
by

## Slide 2: PTP in FTI
Overview:
PTP version 3 in FTI?
Proposal for a PTP profile for FTI

## Slide 3: PTP version 3 for FTI?
The scope of the PTP version 3 working group:
- Correct known technical and editorial errors
- Better accuracy
- Definition of an SNMP MIB
- Security
- Clarify the layering, interfaces and protocol of the standard

## Slide 4: PTP version 3 for FTI?
Don’t panic!
The new revision of the IEEE 1588™ standard will be backward compatible with version 2 and all new functions will be optional

## Slide 5: PTP version 3 for FTI?
IEEE 1588™ has established five sub-committees:
Architecture
High Accuracy
Upkeep
Management
Security

## Slide 6: PTP version 3 for FTI?
Architecture sub-committee
Topic | Description | Relevance for FTI
State reduction | FAULTY, PRE-MASTER and UNCALIBARTED states would become optional | NA, this is implementation specific requirement
Profile isolation | A transport specific attribute in the PTP header is used to isolate multiple PTP profiles in the same network | NA, only one PTP profile should be used in a FTI network
Port State Configuration | A PTP port can be BMCA capable, SC only or GMC/MC only, where manual configuration is possible | NA, all GMC candidates should support BMCA
PTP domains | Multiple PTP domains in a network can share the same timing data | NA, FTI should only allow one PTP domain (default domain)

## Slide 7: PTP version 3 for FTI?
High Accuracy sub-committee
Topic | Description | Relevance for FTI
Synchronization better than 1 nanosecond | Includes support for SyncE Frequency synchronization may be achieved through a different spanning tree than the spanning tree used for PTP Calibration of each SC including compensation for all asymmetric components and cable delays will be part of the proposal A “Golden Calibrator” for a given system may be required. | Data acquisition with sub-nanosecond or single digit nanoseconds accuracy in some future FTI systems may be relevant

## Slide 8: PTP version 3 for FTI?
Upkeep sub-committee
Topic | Description | Relevance for FTI
Upkeep | Incorporate official IEEE interpretations and other known errors or needed clarification into 1588-2008 including clarification on the clarification of the TC source address topic Serve as a “quality control” function for any modifications proposed | NA, no major impact from the Upkeep section is expected for FTI

## Slide 9: PTP version 3 for FTI?
Management sub-committee
Topic | Description | Relevance for FTI
Management protocols | Create a single IEEE 1588 MIB for SNMP management Other management protocols | A standard MIB can be considered for FTI

## Slide 10: PTP version 3 for FTI?
Security sub-committee
Topic | Description | Relevance for FTI
Security capability | Technologies such as IPSec and MACSec are considered Requirements are based on IETF document: “draft-ietf-tictoc-security-requirements | NA, security related to PTP synchronization has not been an issue for FTI up to now

## Slide 11: PTP profile for FTI
Main PTP properties that are relevant for a PTP profile for FTI:
PTP versions
Clock modes
One-step vs. two step clocks
Media
Delay mechanism
Transport mechanism
Domain
Selection of Best Master Clock
PTP EPOCH
Sync interval
Delay_Req interval
Announce interval
PPS output
IRIG-B 002/122
Management
SNMP traps
GMC holdover
SC accuracy
SC time to synchronization

## Slide 12: PTP profile for FTI
PTP versions
  Version 1 according to IEEE 1588™ - 2002
  Version 2 according to IEEE 1588™ - 2008
  Version 3: NA, except for systems with sub-nanosecond requirements
Clock modes
  Grand Master Clock (GMC)
  Ordinary Clock (OC)
  (Boundary Clock (BC))
  Transparent Clock (TC)
  Slave Clock (SC) only
One-step vs. two step clocks
  Only two-step

## Slide 13: PTP profile for FTI
Media
  Ethernet
  10/100BASE-T(X), 100BASE-FX, ), 1000BASE-X and 10GBASE-X, etc
  Full Duplex
Delay mechanism
  E2E
Transport mechanism
  PTP over UDP/IP
  Multicast with destination IP address: 224.0.1.129
  UDP destination port number 319 (event packets) and 320 (general packets)

## Slide 14: PTP profile for FTI
Domain
  Default domain (0)
Selection of Best Master Clock
  Default BMCA (mandatory)
PTP EPOCH
  TAI

## Slide 15: PTP profile for FTI
Sync interval
  [1, 2] seconds for IEEE 1588™ - 2002, where:
  1 second is default Sync interval for IEEE 1588™ - 2002
  [0.125 .. 2] seconds for IEEE 1588™ - 2008, where:
  0.125ms is default Sync interval for IEEE 1588™ - 2008
Delay_Req interval
  60 seconds with randomization for IEEE 1588™ - 2002
  [Sync interval, 32 x Sync_interval] seconds with randomization for IEEE 1588™ - 2008
Announce interval
  1588™ - 2002: NA
  1588™ - 2008: 2 x Sync interval

## Slide 16: PTP profile for FTI
PPS output
  Mandatory for;
    GMC
    OC
    (BC)
    TC/SC
    SC
IRIG-B 002/122
  Mandatory for;
    GMC
    OC
  Optional for;
    TC/SC
    SC

## Slide 17: PTP profile for FTI
Management
  Mandatory:
    iNET SNMP and MDL
  Optional:
    PTP management according to chapter 15 of IEEE 1588™ - 2008
    Private MIB or MIB based on PTP version 3?
PTP management
based on
PTPv2Browser,
monitoring
OffsetFromMaster

## Slide 18: PTP profile for FTI
SNMP traps
  iNET SNMP traps, ref TmNS MIB:
    timeLockLostNotificationBranch
    ieee1588MaxOffsetFromMasterNotificationBranch
    ieee1588MaxJitterNotificationBranch
GMC holdover
  0.1ppm (iNET requirement)
CM1608F0-AERO-GMC, clock drift over 60 minutes with temperature cycling: -40˚F/-40˚C to 203˚F/95˚C

## Slide 19: PTP profile for FTI
SC accuracy
  1ppm (iNET requirement)
SC time to synchronization
  1 seconds for airborne systems (iNET requirement)
  3 seconds for ground installations (iNET requirement)

## Slide 20: PTP profile for FTI
 | IEEE 1588™ - 2002 FTI PTP profile | IEEE 1588™ - 2008 FTI PTP profile
Clock modes | OC (GMC), TC(*), Slave only | OC (GMC), TC, Slave only
One-step or two step clocks | Two-step | Two-step
Media | Ethernet, full duplex according to IEEE802.3 | Ethernet, full duplex according to IEEE802.3
Delay mechanism | E2E | E2E
Transport mechanism | PTP above UDP/IP, multicast with destination IP address: 224.0.1.129 and UDP destination port number 319 (event packets) and 320 (general packets) | PTP above UDP/IP, multicast with destination IP address: 224.0.1.129 and UDP destination port number 319 (event packets) and 320 (general packets)
Domain | Only default domain (0x00) is used | Only default domain (0x00) is used
Selection of Best Master Clock | Default BMCA algorithm | Default BMCA algorithm
PTP EPOCH | Time representation based in TAI, offset to UTC time (accumulated number of leap seconds) is defined in the currentUTCOffset parameter. | Time representation based in TAI, offset to UTC time (accumulated number of leap seconds) is defined in the currentUTCOffset parameter.
Sync interval | [1, 2]s, default = 1s | [0.125 .. 2]s, default = 0.125s
Delat_req interval | 60s, randomized | [Sync interval .. 32]s, default = 32s, randomized; controlled by GMC
Announce interval | NA | [1, 2, 4, 8, 16]s, default = 2s
PPS output | Mandatory | Mandatory
IRIG-B 002/122 | Mandatory for GMC Optional for TC/SC | Mandatory for GMC Optional for TC/SC
Management | iNET SNMP/MDL | iNET SNMP/MDL Optional: PTP management according to IEEE 1588™ - 2008
SNMP traps | iNET MIB | iNET MIB
GMC holdover | 0.1ppm, iNET requirement | 0.1ppm, iNET requirement
SC accuracy | 1ppm, iNET requirement | 1ppm, iNET requirement
SC time to synchronization | 1s/3s (airborne/ground), iNET requirement | 1s/3s (airborne/ground), iNET requirement

## Slide 21: Questions?